## Slide 1: Accelerating Gene Sequencing with FPGA technology
Meysam Roodi
David McTavish
Arash Moghimi
Leon Xiang Li

## Slide 2: Project Overview and Goals
Implementing a gene sequencing system
FM-index algorithm is used for sequencing
The goal is to do EXACT sequence matching

## Slide 3: Original Block Diagram

## Slide 4: Updated Block Diagram

## Slide 5: Design Environment
Partitioned project into four distinct parts in order to make version control software unnecessary
1. Set up Linux on hardened ARM processor and interface with programmable logic’s external memory
2. Developed software that could complete Burrow –wheeler transform
3. Developed HLS module that could perform FM index to find short reads in gene sequence
4. Set up interface between DDR memory and HLS module

## Slide 6: Design Environment for Petalinux
Parts 1 and 4 required “Petalinux Tools” which was only available for a Linux Operating System
Vmware was used to run Linux in a virtual machine

## Slide 7: Design Environment for Petalinux
Once Petalinux was booted off of SD Card the hardened ARM processor could communicate with a connected PC using Tera Term

## Slide 8: Design Environment for Programmable Logic
Required Vivado Studio to create a block diagram of the system

## Slide 9: Design Environment for Hardware Accelerator
HLS was used to develop the hardware accelerator that could perform the FM indexing

## Slide 10: Testing and Verification of BWT Algorithm
Both the C-table and I-table are based on the transformed sequence, therefore, the most important task is to verify the correctness of the transformed sequence.
We first tested the software by transforming a short sequence from a paper
Then for longer sequences, we tested the transformation using an online BWT transformation software as a reference. http://kodu.ut.ee/~lipmaa/research/bwt/

## Slide 11: Testing and Verification of BWT Algorithm (cont’d)
Original reference sequence | Transformed sequence (BWT software) | Transformed sequence (online software)
GCTAATTAGGTACC$ (14) | CTTTACAG$AGCGTA | CTTTACAG$AGCGTA
ACAATTCTTATGCGATTATGGCATATCGATCGATGCATTCGATCGATGCA$ (50) | ACC$CTGGGGTTGCAGAGGTTTTGTCCCCCTGTTTATTTAAATAAAACAAA | ACC$CTGGGGTTGCAGAGGTTTTGTCCCCCTGTTTATTTAAATAAAACAAA
ATCGATGCATGCATGCATCTAGCACGATCAGTCGATCGATCGATGCATCAGTCATGATAGCATCAGTTAGAATTATAAATGCGGCGCCTCCCTATATATATTATATAGCAGCTAGCGCGCTCCCTCTCTTCCCCTTAGATTAGCATGCATTATGGATCTGTAGTAGCATATGCTACTTCAGTCAGTAGCTAGCTAAATGC$ (200) | CTTAAGCTTTTTTTTTTCTTCCCCCTTGTTTCTCGCGG$CGCAGCCGCATTGATCGGGTTTTTGGGGTGGGGTTTCCGCCATTTTGGGGGGTGGCCGCTTCATATCCCGCCATAAATATTTATCGACTATAACTCAATAAAACACTTCAGATCCGGTATCAAATAGTAAAGTCCGAAAACACAAAAAAAAAACGCAAAACC | CTTAAGCTTTTTTTTTTCTTCCCCCTTGTTTCTCGCGG$CGCAGCCGCATTGATCGGGTTTTTGGGGTGGGGTTTCCGCCATTTTGGGGGGTGGCCGCTTCATATCCCGCCATAAATATTTATCGACTATAACTCAATAAAACACTTCAGATCCGGTATCAAATAGTAAAGTCCGAAAACACAAAAAAAAAACGCAAAACC

## Slide 12: Verification of External Memory Writes
Checked what was written in each 32 bit address after each write

## Slide 13: Verification of HLS block
A C test bench to verify the functionality of HLS block
C and I tables are read by the test bench and loaded into arrays
The HLS sequencer block is commanded to start the sequencing

## Slide 14: Verification on ITX Board
Used the same reference sequences and short reads as previous steps
Could peek/poke the physical memory directly, allowing us to ensure the processor’s writes to memory were correct
Added additional slave registers to the HLS module, to contain extra information if there was an error (eg. Did not read a correct character in a short read)

## Slide 15: HLS module: The actual sequencer
The actual sequencer is implemented in Vivado HLS

## Slide 16: Benefits of Using Vivado HLS
Fast implementation time
No need for test bench development
Fast interface development
(Vivdao and Vivado HLS) very effective and fast integration
Automatic handshake development (AXI)

## Slide 17: Vivado HLS vs. HDL development
The design and testbench development time difference
Design HDL implementation details
  Handshake/interface development
  FSM/datapath design and implementation
Test bench development
  Memory Model
  Data injection, collection, checkers
Totally at least 5x longer

## Slide 18: Overall Vivado HLS impression
+ Points
  Very easy to use
  Fast development and verification
- Points
  Sometimes directives do not behave as expected
  Sometimes more control is needed by the designer over a piece of code (Verilog in C, like ASM in C)
  Translated HDL is not readable/verifiable

## Slide 19: Impact of HLS on Interfacing
Already provided control signals and easy interfacing over AXI, and adding of any new slave registers
Having master AXI ports (with offsets you can specify in a slave register) allows easy selecting and accessing of memory (particularly the DDR via the MIG)

## Slide 20: Demonstration
3 short reads
Expected Results:
  Match
  No match
  Match